## Slide 1: Study, modeling and simulation of pedestrian walk with regard to the improvement of stability and comfort on walkways
Pavlos Paris Giakoumakis
AM:
School of Electrical & Computer Engineering
Implementation Report
Thesis project - Erasmus+ internship at University of Modena & Reggio Emilia (UNIMORE)

## Slide 2: Goals
Calibration of the database that consists of valid measurements for 215 pedestrians
Extraction of the appropriate variables describing the human gait
Statistical modeling of variables taking all database samples into consideration
Extraction of statistical model of parameters
Development of a gait simulator based on the statistical model – Extraction of variables for a defined number of steps

## Slide 3: The Database
Includes measurements of traverses in a m walkway for pedestrians in a variety of physical characteristics in a normal walking tempo
Includesx cells – is the maximum number of steps each pedestrian performs in walkway traversals
Each pedestrian’s step (cell) contains:
  Vertical force applied to the floor ()
  Time that the foot came in contact with the ground ()
  Contact coordinates in and axes (, )
Depiction of and axes

## Slide 4: The Database - Example

## Slide 5: Variable Extraction
Computation of each step’s necessary variables based on the database samples
  Interarrival time between steps ()
  Mean vertical force induced in the floor on each step (mean force)
  The traversed distance between steps (length)
  The step angle along the gait horizontal direction (angle)
Extraction of unified table X (xx)
Dt-meanF-length-angle
Pedestrians
Steps

## Slide 6: Variable Modeling
Use of Gaussian Mixture Models (GMMs)
  No correlation of step angle (angle) with the other three random variables has been reported
  Correlation between Dt – Mean force – length
  A GMM of X components has been fitted in the variables added to a GMM of X components for the step angle - GMMs in total (x)
  The GMMs describe the distributions successfully as proved by the use of the two-sample Kolmogorov-Smirnov test
Each GMM is characterized by parameters:
  Mean table (mu): components x variables vector (x for the variables or x for the angle)
  Mixing probability – component proportion: array in the size of the GMM’s component number (5 or 3) – summed to , describes the a-posteriori estimates of the component probabilities
  Covariance matrix (Sigma): Symmetric and positive semi-definite vector describing the covariance between variables των μεταβλητών. Size: variables x variables (x ή τιμή)

## Slide 7: Parameter Modeling
Modeling the GMM parameters in order to extract a complete statistical model that describes the human gait
  GMMs have been used for the parameter modeling once again
Modeling mu:
  Separate GMMs for each variable’s mu have been fitted
  One GMM for each component of each variable
  Unification and sorting of mus in order to acknowledge the small values
  Therefore, GMMs have been fitted for each of the variables Dt, meanF, length and GMMs for the angle – Total: GMMs for the mu modeling

## Slide 8: Parameter Modeling
Modeling mixing probability – component proportion:
  A GMM describing the component proportion of each component has been fitted
  Correlation with mu values – During mu’s sorting, the proportions are shifted to correpsond to the components mus
  Thus, GMMs describing the variables Dt, meanF, length and GMMs for the angle have been fitted – Total: 8 GMMs to describe the component proportion
Modeling Sigma:
  A GMM for each critical value of Sigma has been fitted, i.e. for GMMs describing variables, ax matix containing 6 critical values is required
  6 critical values: the matrix diagonal and the covariances between 1st -2nd, 1st - 3rd and 2nd - 3rd variable
  Unified covariance matrices containing the critical values have been created
  Concluding, 6 GMMs describing the variables Dt, meanF, length and GMM GMMs for the angle have been fitted – Total: GMMs to describe Sigma

## Slide 9: Modeling mu - Logic
Modeling mean values of the components describing
  The same procedure is followed for meanF, length
  Each first column’s values are corresponding to the mean value of each component describing
  Modeling each of the values describing each variable
  Initially, ascending sorting of the variable’s mean values is performed

## Slide 10: Modeling mu - Logic
  Each element is distributed in a corresponding array
  arrays containing the mus of each GMM are created – ascending order
  A GMM of components is fitted in each array
  Total: GMMs modeling the mus of Dt
  Hence, it is ensured that the low mus’ vaules are not ignored during the modeling
  Modeling angle in a similar logic – Use of GMMs

## Slide 11: Modeling mu - Implementation
  A common x mu vector that includes each component’s mu values is created for each GMM ( variable)
  Ascending sorting of rows is performed
  A component GMM is fitted in each row

## Slide 12: Modeling mu - Plot

## Slide 13: Modeling Mixing Probability - Logic
  During the sorting stage of mu modeling, the mixing probability values are shifted to correspond to the sorting’s modified indexes
  Each element is allocated in an array in the same manner as mu’s modeling
  A GMM of components is fitted in each array –
  Total:components modeling mixing probability
  Hence, the correspondence with each component mus is ensured
  Modeling angle in a similar logic – Use of GMMs

## Slide 14: Modeling Mixing Probability – Implementation
  A common x weight vector containing mixing probabilities of each component for each GMM is created
  Index pairing based on mu’s sorting is performed
  A GMM of components is fitted in each row

## Slide 15: Modeling Mixing Probability – Plot

## Slide 16: Modeling Sigma - Logic
  Symmetric X matrix – 6 critical values
  Each variance/covariance value is matched to an array
  A GMM of components is fitted in each array
  Total: 6 GMMs modeling Sigma
  Angle: GMM in variance values is fitted

## Slide 17: Modeling Sigma – Implementation
  A common x6 Sigma vector containing the variable variance/covariance values is created for each GMM
  A GMM of components is fitted in each row

## Slide 18: Modeling Sigma- Plot

## Slide 19: Modeling Overview
Variable Extraction
Variable Modeling
Parameter Modeling

## Slide 20: Developing a Simulator
Extraction of the variables describing a gait of steps based pm the statistical model
A reversed procedure is followed
  The parameters (mu, mixing probabilities and Sigma) are generated randomly using the GMMs describing them
  A GMM is fitted using the generated parameters. This GMM constitutes the distribution that describes the human walk
  n sets of variables(Dt, meanF and length) are generated using this GMM
  The same procedure (fitting of one more GMM) is performed in order to extract the step angle using the corresponding GMMs describing these parameters

## Slide 21: Parameter Extraction
Extraction of the mean table (mu)
  random values are generated using the GMMs
  The generated values constitute the mu parameter of the GMM describing the variables
Extraction of mixing probability – component proportion array:
  random values are generated using the GMMs
  These generated values constitute the mixing probability parameter of the GMM describing the variables
  A normalization of the values is conducted in order to sum to
  For the extraction of mus and mixing probabilities describing the angle of step, the 6 GMMs are used respectively for the extraction of thevalues of each parameter

## Slide 22: Parameter Extraction
Extraction of the variance/covariance table (Sigma)
  Using the GMMs describing Sigma, random values are generated for
  The first values constitute the matrix diagonal, while the values remaining describe the covariances between the variables
  This procedure is repeated until a symmetric positive semi-definite matrix is generated
  For the extraction of Sigma describing the angle of step, the counterpart GMM describing it is used

## Slide 23: Extraction of Random Walk
GMMs are fitted using the generated parameters
random sets of variables are generated using these GMMs (Dt, meanF and length using the st and angle of step using the nd)
The join of those sets describes a random walk of steps

## Slide 24: Evaluation of Simulation
The simulated results approach the experimental quite effectively
  Notable difference in the mean force values due to different body types affecting the measurements
  The mean velocity of the simulated gait has been calculated as . This values approaches the mean velocity of human walk at a normal tempo
  The two plots depict the simulated gait in comparison to the experimental
Innovative approach
  No other research work has used GMMs for the modeling of human walk
  First work that conceives the human walk as a random process
  Uses large amount of experimental samples
Thus, using this approach, the experimental procedure can be omitted in future researches

## Slide 25: Future Goals
Apply the simulator in a digital pedestrian walkway developed by the Civil and Environmental Engineering Department of University of Modena & Reggio Emilia (Dipartimento di Ingegneria "Enzo Ferrari”) in order to conduct research on bridge oscillations and the resonance effect
Publication of research paper that includes this work